## Slide 1
Robust Registration of Longitudinal Spine CT
Ben Glocker1, Darko Zikic2 , David R. Haynor3
1Biomedical Image Analysis Group, Imperial College London, UK 2Microsoft Research Cambridge, UK 3University of Washington, Seattle, USA
Longitudinal Registration
Challenge: Fully automatic, robust initialization
Robust initialization is a major challenge for automatic methods
Pre- and post-operative scans can vary significantly, e.g. small overlap
Shape differences after treatment of deformities, e.g. scoliosis
Appearance differences due to surgical implants, e.g. metal screws
Solution: Use of location priors during registration
Learning-based extraction of semantic information from images
Location priors provide patient-specific coordinate system
Priors are used to initialize the registration and guide the optimization
Integrating priors significantly reduces the number of failure cases
Localization Priors via Classification
Glocker et al. “Vertebrae Localization in Pathological Spine CT via Dense Classification from Sparse Annotations”. MICCAI 2013
Dense Labels from Sparse Annotations Generate training data for learning a dense classifier
Centroid Estimation from Dense Classification Voxel-wise classification, mean shift, and outlier removal
Training
Testing
Annotations
Dense Labels
Annotations
Dense Labels
Classification
Outlier Removal
Classification
Outlier Removal
T3
C6
T3
C6
Fixed
Moving
Vertebrae Location Priors
Registration Procedure
1. Prior-based Initialization
2. Rigid Registration
3. FFD-based Non-rigid Registration
Prior-based Registration Objective Incorporating priors into optimization problem
Quantitative Evaluation
Initialization with different methods
Contact: b.glocker@imperial.ac.uk
T3
C6
Priors
1D Exhaustive
Centers of Mass
Fixed
Moving
Moving
Moving
Clinical Spine CT Dataset* *available on http://research.microsoft.com/spine
CT scans from 93 patients
A total of 276 registrations
pre- and post-operative scans
limited view, 5-15 visible vertebrae
include high-grade scoliosis, kyphosis, fractures, implants
manual annotations of all vertebrae centroids available
Baselines for Comparison
‘Centers of Mass’: pre-aligns centers of intensity masses
‘1D Exhaustive’: exhaustive search along the main anatomical axis
Computational Efficiency
Intel Xeon 3.5GHz, C# implementation
Registration including prior computation takes 2 min
Statistics of registration errors for different methods
Images
Prior Maps
Detected Vertebrae
Intensity-based objective
Prior-based objective
Visual registration examples
Moving
Registered
Fixed
Moving
Registered
Fixed